## Slide 1: Developing Controllers for Biped Humanoid Locomotion
Yariv Bachar
21st July, 2004

## Slide 2: Presentation Outline
Project Description
The Zero Moment Point
Project Architecture
Methodology
Key Challenges
ZMP Jacobian Counterbalance
Demo
Significance
Future work

## Slide 3: Project Description
Motivation: Dynamically stable locomotion is essential for developing real-world humanoid robots.
Key challenge: Devise a control scheme which ensures robust and stable walking pattern.
Principle goal: Develop a natural looking walking gait for a 22DOF humanoid robot simulation with full-contact physics.
Incorporate Zero Moment Point (ZMP) control for generating dynamically stabled walking.

## Slide 4: The Zero-Moment Point
Definition: point on ground, about which net moment of inertial forces and gravity forces has no component along the horizontal plane.

## Slide 5: The Zero-Moment Point II
Support Polygon - the convex hull of the foot support area.
If ZMP inside support polygon  system is dynamically balanced.

## Slide 6: Calculating the ZMP
which becomes:
The ZMP has to satisfy:
where:
  p = [ xZMP , yZMP , zZMP ] : the ZMP.
  n : number of links.
  mi : mass of link i.
  Ii = diag( Iix , Iiy , Iiz ) : link i’s inertia tensor.
  g = [ 0 , 0 , -g ] : gravity acceleration.
  ri = [ xi , yi , zi ] : link i’s center-of-mass.
  ωi : link i’s angular velocity.
  M = [ Mx , My , Mz ] : moment around ZMP.
constant
computed
dynamically

## Slide 7: Project Architecture
Robot Model
  Based on Sony QRIO.
World and Physics Model
  Friction, Gravity, Mass, etc.
Controller:
  Balance Algorithms.
  Motion Generation.
  Supervisor.
  Input/Output (Visualization/Statistics).

## Slide 8: Methodology
WebotsTM mobile robotics simulation software.
Programming in C/C++ on Linux Platform (also IPC).
Open Dynamics Engine (ODE) - rigid body dynamics simulation library.
CGAL - Computational Geometry Algorithms Library written in C++.
Arabica – a C++ XML parser toolkit, providing SAX2 and DOM implementations.

## Slide 9: Key Challenges
The “Inverse problem”:
  “Given a stable ZMP trajectory, produce joint trajectories”.
Full access to dynamic information in Webots:
  Most dynamic stability algorithms require: mass, inertia, angular velocity per link.
    Collaboration with Olivier Michel and Pascal Cominoli (EPFL – Switzerland).
Motion pattern generation:
  How to get basic motion data to work with.

## Slide 10: ZMP Jacobian Counterbalance
Overview: adapts humanoid predefined walking trajectories to reduce the deviations in dynamic stability criteria, in terms of the ZMP  Improves walking performance.
Note: can be generalised to other task-dependent Cartesian deviations (e.g. specific joint position coordinates, CoM Cartesian position).

## Slide 11: The ZMP Jacobian Concept
The ZMP’s position, pZMP, is a function of the system’s joint angles q:
To modify pZMP,, by ∆pZMP in 3D space  modify the joint angles vector q by:
This f(•) relationship is a Jacobian matrix:
This Jacobian, a function of the “actual” joint angles qa, maps the velocity vector in joint-space to ZMP velocity:

## Slide 12: ZMP Compensation Pseudo-code
The Counterbalance is done using specific joints, i.e. only those joints trajectories are adapted.
  Ideally, these should be the redundant joints.
  The more joints used  more computation!
The adaptation is performed iteratively, modifying only a fraction of the desired change.
Those modifications are accumulated to create a final, more balanced motion.
Also, the local neighborhood of the changes are interpolated – smoothed!

## Slide 13: Convergence Issue

## Slide 14: Humanoid Motion Generation I
Problem: Automatic generation or planning of full-body motion for humanoids is a complex computational challenge:
  Large number of DOFs.
  Intricate kinematic and dynamic models.
  Stability.
Strategies:
  Motion generation applications with rich GUIs.
  Human motion capture using optical tracking devices.
  Generation relied on kinematics/dynamics models (obstacle avoidance).

## Slide 15: Humanoid Motion Generation II
The approach: motion definitions, specifying via points per joint + time frame sequence corresponding to these via points.
Trajectory Interpolation:
  Essential to apply smoothness, otherwise motions would result in “bang-bang”.
  Motions defined only in positional terms  produce unstable/undesirable motion.
  Given motion definitions, interpolate the joint angle values within each two via points in the sequences.
<?xml version="1.0" encoding="UTF-8" ?>
<GLOBAL_DEF>
  <DEFINE>
    <JOINT_DEF number="0"> joint_0_name </JOINT_DEF>
    …
    <JOINT_DEF number="n"> joint_n_name </JOINT_DEF>
  </DEFINE>
  <MOTION_DEF>
    <SEQ id="FIRST_STEP" comment="Start from standing; right leg forward">
      <JOINT id="joint_i_name"> 0.2 0.15 0 </JOINT>
      …
      <JOINT id="joint_m_name"> -0.3 -0.3 -0.3 </JOINT>
      <TIME_DEF type="interval"> 0.512 </TIME_DEF>
    </SEQ>
    …
  </MOTION_DEF>
</GLOBAL_DEF>

## Slide 16: Time for a Demo
Sit back and enjoy ….

## Slide 17: Significance
Independence of feet-ground contact states.
An assurance that the ZMP can characterise the humanoid’s global dynamics.
  ZMP can be utilised for legged robots controller design.
Pedantic description of the development of a simulated humanoid locomotion controller.
  Large engineering contribution.
  Combination of sophisticated humanoid simulation with ZMP based locomotion.

## Slide 18: Future Work
The method (relating ZMP to dynamic balance control).
  Analytically developing the ZMP Jacobian.
The implementation.
  ZMP Jacobian Approximation (e.g. recursive regression learning).
The experiments/applicability of proposed method.
  Applying to various humanoid models.

## Slide 19: Future Work
The method (relating ZMP to dynamic balance control).
  Analytically developing the ZMP Jacobian.
The implementation.
  ZMP Jacobian Approximation (e.g. recursive regression learning).
The experiments/applicability of proposed method.
  Applying to various humanoid models.